| Max Spark Rate: Multi Spark Restrike Rate: | > 1.2 KHz > 1.2 KHz |
| --- | --- |
| Output Energy: Per ignition event to coil (& open circuit voltage) Low o/p setting High o/p setting | 126 milli joule (450 volts) 160 milli joule (505 volts) |
| Trigger Iutputs Type | 10mA Open collector drive |
| Supply Voltage Operational range Range for operation to 16000 rpm (8cyl) Safe limits | 6.2 to 20 volts > 12 volts +/- 24 volts (5 min) +/- 80 volts (alternator load dump 0.5 sec) +/-1000 volts (inductive spike 10usec) |
| Current Drain Shutdown Engine stopped @ max spark rate | < 10 uAMP < 200 mAMP < 13 AMP |
| Temperature Range Storage Operating | -25 to 100 deg C -25 to 85 deg C |
| Size Case Overall | 180 *140 * 50 mm 200 *140 * 50 mm |
| Weight | 0.75 Kg |